## Slide 1
Status of the Radiometric Calibration Network: RadCalNet
M. Sinclair on behalf of M. Bouvet and the RadCalNet WG (CEOS/WGCV/IVOS)

## Slide 2
What is RadCalNet?
Site X
RadCalNet portal
Calibration
& QC
& Processing
Raw measurements
Surface reflectance and atmosphere products
(RadCalNet specific)
FTP
FTP
RadCalNet
Processing
&
QC
Hyperspectral TOA reflectance @ 30 mins interval for nadir view
Site Y
Calibration
& QC
& Processing
Raw measurements
Surface reflectance and atmosphere products
(RadCalNet specific)

## Slide 3
The RadCalNet sites
BTCN + BSCN
GONA
RVUS
LCFR
Today 5 sites (+ more in preparation)

## Slide 4
RadCalNet
Processing (RTM)
Surface reflectance
Atmospheric measurements
TOA reflectance
The data processing

## Slide 5
The portal

## Slide 6
Forum

## Slide 7
Data availability overview
The full archive provide more than 7000+ days worth of data from the 5 sites and spanning 13 years. Both ASCII and NetCDF format available
Data availability (requirement: > 90 days / year) generally constrained by weather conditions for non desertic sites.
Data latency (requirement: <2 weeks from acquisition) remains a challenge for several sites
Limited instrument availability at Gobabeb in 2025
Operation at Batou should resume in Q2 2026 (like every year after winter).
Number of days/year with RadCalNet data availability at each site

## Slide 8
2025 collection release
RadCalNet archive updated on 3rd of Nov 2025
Full reprocessing of Railroad Valley Playa data:
  New NO2 and CH4 input data from Sentinel-5P TROPOMI
  Usage of AERONET Level 1.5 aerosol optical depth (rather than Level 2 data)
  The TSIS-1 v2 HSRS extraterrestrial solar spectrum rather than the Thuillier spectrum.
Reprocessing/modification of only few isolated dates for La Crau, Gobabeb and Baotou.

## Slide 9
Quality control: an example with GONA atmospheric data

## Slide 10
Quality control: LCFR surface reflectance

## Slide 11
Comparison of Sentinel 2A to RadCalNet TOA at Railroad Valley Playa over archive
RadCalNet TOA reflectance available every 30 mins
Sampled at 10 nm spectral sampling interval
S2A geometry is not exactly nadir
BRDF effects not accounted for

## Slide 12
Site Intercomparison – 5 sites spectral synthesis
S2 vs RadCalNet TOA reflectance
L8 vs RadCalNet TOA reflectance
NB: S2/L8 spatial resolution NOT compatible with Baotou artificial target size (=BTCN).

## Slide 13
Acceptance process for new sites
Candidate site owners provide 45+ days worth of data, a site description and document their uncertainty budget.
RadCalNet WG members review and a dedicated panel provides final recommendation for acceptance
Final assessment and acceptance by CEOS/WGCV

## Slide 14
Upcoming sites
Figure 10: GHNA ASD Site Survey Line March 2020, GHNA mast marked in centre of fence square.
Figure 2: GoogleEarth site zoom
3 new sites have submitted their application to RadCalNet
Already prepared a 45+ days of data and site description and uncertainty statements
All gone through two rounds of review and comparisons to S-2 / Landsat data
From left to right: USGS EROS center (US), HYPERNETS Gobabeb (Namibia) and Golmud (China)

## Slide 15
Oceanic sites for RadCalNet – in preparation
Match up comparison Sentinel-2 from 2017 to 2024 at Venice Tower
Development of a processing chain starting from AERONET-OC multipspectral water leaving radiance, generating hyperpespectral water leaving remote sensing reflectance (Rsr) and then TOA reflectance at RadCalNet geometry and temporal sampling.
Expected to be submitted for acceptance for Venice Tower (Italy) and Galata platform (Roumenia)

## Slide 16
New Sites Status
Initial concept
Identify location
Set up instruments
Collect data
Prepare draft documents
Prepare submission
Submit application to RadCalNet
First Review
Second Review
Acceptance
Operation
BTCN
BSCN
GONA
LCFR
RVUS
PIAU
DHCN
GHNA
ERUS
AERONET- OC sites
GSCN

## Slide 17
Users

## Slide 18
Users
18/05/2026
18
71 countries
Top 3 : US, China, South Korea

## Slide 19
Conclusion
8 years of RadCalNet operation
5 sites currently providing data and 3 new sites about to join the network
Golmud submitted for acceptance to WGCV
New 2025 data collection available
An archive spanning 13 years and cumulating 7000+ days of data for EO sensor radiometric assessment
Continuous efforts to maintain data quality and improve timeliness of data
Growing user base

## Slide 20: Thank you